## Slide 1: Smart head-mounted LED lights
Nicolas Fouque , WANG Zhe,HE Puyuan

## Slide 2: 1. Project description
Achieve uniform illumination of the target plane by adjusting the LED light array, even if there are random effects from external light sources.
3x3 LED array
& 3x3 photodiode array

## Slide 3: 2. System overview
Our system
Height,angle
Automatic measurement
Expected luminance of the target surface
By smart phone
and bluetooth
The distribution of luminance of the target surface
By photodiodes
Modified by the LED array

## Slide 4: 3. LED lighting module
the regional distribution of light intensity on the ground when and h=0.3m,1m and 1.7m(from left to right)
the regional distribution of light intensity on the ground when h=0.3m and (from left to right)
Results of simulation:
By using Matlab we can know the area that can be illuminated on the target surface

## Slide 5: 4.Automatic distance and angle measurement module
MPU9250
3-axis gyroscope,
3-axis accelerometer,
3-axis magnetometer
Sharp GP2Y0A41SK0F
We can use it to measure the angle of inclination

## Slide 6
5. Detection system
Physical model: 3*3matrix like LED and Flux collet system
Photodiode : SFH230

## Slide 7
5. Detection system
Trying to reduce the high frequency noise
Using a pow-pass filter to process the data
Final result : the average of the data after the filter ( the 9 photodiodes )

## Slide 8
6. Feedback correction module
Adjust the Luminance of LED according to the difference between the target value and measurement value
We have the final result of the nine targets place (every led is in charge of one place )

## Slide 9
7. Interface Utilisateur

## Slide 10
8. Design and Improvement
Compact the device and try to use only one Nucleo
Translate the code in C++ in order to don’t use MATLAB because it’s require a computer
Check the power of this system
Test with other matrice component
Improuve the performance with a Optic design study and lense